## Slide 1
Enterprise Data Center
Storage Architecture
NAS · SAN · Fibre Channel · SAN Switches
Presented by: Navdeep Audience: Arun Purpose: In-depth Enterprise Storage Understanding

## Slide 2
AGENDA
Session Overview
1
What is Storage in a Data Center?
2
Why Enterprises Use Dedicated Storage
3
Storage Architecture Types (DAS / NAS / SAN)
4
NAS – Concepts, Protocols & Use Cases
5
SAN – Concepts, Block Storage & Use Cases
6
Fibre Channel Overview & Components
7
SAN Switches, Zoning & Multipathing
8
NAS vs SAN Comparison Table
9
Real-World Enterprise Storage Design
10
Summary & Key Takeaways

## Slide 3
What Is Storage in a Data Center?
Storage is the core infrastructure layer that permanently preserves enterprise data — including applications, databases, virtual machines, logs, backups, and files — independently of compute servers.
Persistent Storage
Data survives server reboots, failures, and replacements without loss.
Network Accessible
Multiple servers access shared storage over dedicated high-speed networks.
Centrally Managed
Unified management, security policies, snapshots, and capacity planning.
KEY PRINCIPLE: Even if a server fails, data must remain safe, accessible, and consistent.

## Slide 4
Storage Architecture Types
Three distinct models — each suited to different performance, cost, and scalability requirements.
DAS
Direct Attached Storage
Storage directly wired to one server. Fast for that server alone — not shareable. Used for OS disks, small apps, test environments.
Single-server only
SATA / SAS disks
No networking
Limited scalability
NAS
Network Attached Storage
File-level storage delivered over standard Ethernet. Appears as a shared folder. Uses NFS (Linux) or SMB/CIFS (Windows).
File-level access
Ethernet-based
Easy to deploy
Shared by many servers
SAN
Storage Area Network
Block-level storage on a dedicated high-speed fabric. Presented as a raw disk to each server. Ideal for databases and VMs.
Block-level access
Dedicated FC fabric
Highest performance
Mission-critical apps

## Slide 5
NAS – Network Attached Storage
NAS ARCHITECTURE
Clients / Servers
Ethernet Switch
NAS Controller
Disk Pool
NFS (Linux) · SMB/CIFS (Windows) · HTTP/S3
File-Level Access
NAS manages entire files and directories. Clients use standard file system calls — no raw disk access.
Protocols
NFS for Linux/Unix · SMB/CIFS for Windows
Traffic travels over standard Ethernet (1G / 10G / 25G).
Use Cases
File servers · Home directories · Application logs
Media storage · Collaboration platforms
Benefits
Easy to deploy · Cost-effective · Centralized sharing
Supports heterogeneous OS environments

## Slide 6
SAN – Storage Area Network
SAN ARCHITECTURE FLOW
Server
HBA
SAN
Switch A
SAN
Switch B
Storage
Controller
Disk
Pool / LUNs
Fibre Channel (FC 16G/32G) or FCoE over dedicated fabric
Block-Level Access
Storage presented as raw disk (LUN) to server. OS formats & manages file system. Maximum flexibility.
HBA (Host Bus Adapter)
Specialized PCIe card in the server with a Fibre Channel port. Handles FC protocol offloading from CPU.
LUNs (Logical Units)
Logical partitions inside the storage array. Each server maps one or more LUNs as its own local disk.
Use Cases
Oracle/SQL databases · VMware vSphere VMs
High-transaction systems · Mission-critical apps

## Slide 7
Fibre Channel (FC)
The gold standard for high-performance, low-latency storage networking
FC SPEED EVOLUTION
1G
2G
4G
8G
16G
32G
64G
128G
← Legacy Current Enterprise Standard → Future →
HBA
(Host Bus Adapter)
Plugs into server PCIe slot. Has 1-4 FC ports. Offloads FC protocol from CPU for zero-latency performance.
FC SFP+
Transceivers
Short-range (SW) or long-range (LW) optical modules. Plug into HBA ports. Carry light pulses over fiber.
Fiber Optic
Cables
OM3/OM4 multimode for rack-scale (up to 100m). OS2 singlemode for inter-building long-distance runs.
FC Switch
Port / ASIC
Every FC switch port runs full-duplex, non-blocking fabric. Buffers large frames for lossless delivery.

## Slide 8
SAN Switches, Zoning & Multipathing
DUAL FABRIC TOPOLOGY
Server (HBA A + HBA B)
SAN Switch A
Fabric 1
SAN Switch B
Fabric 2
Storage Array
(Dual Controller)
Path A (active)
Path B (standby / load-balance)
What Is a SAN Switch?
Specialized Fibre Channel switch that builds the storage fabric. Connects servers and arrays into a switched, non-blocking network.
Vendors: Brocade (HPE/IBM), Cisco MDS Series.
Zoning
Zoning restricts which servers can 'see' which storage. Implemented at the switch level using WWNs (World Wide Names).
• Hard Zoning: enforced in hardware (recommended)
• Soft Zoning: name-service based
Benefit: Security + prevents accidental data access.
Multipathing (MPIO)
Multiple physical FC paths between server and storage array.
• Automatic failover if one path goes down
• Load balancing across both paths
• Software: MPIO (Windows), DM-Multipath (Linux)
Benefit: Zero downtime, higher throughput.

## Slide 9
NAS vs SAN – Side-by-Side Comparison
Attribute
NAS
SAN
Access Type
File-level (files & folders)
Block-level (raw disk LUNs)
Protocol
NFS (Linux), SMB/CIFS (Windows)
Fibre Channel, iSCSI, FCoE
Network
Standard Ethernet (1G/10G/25G)
Dedicated FC fabric (16G/32G/64G)
Performance
Good – suitable for file workloads
Excellent – sub-ms latency
File System
Managed by NAS controller
Managed by the OS on each server
Cost
Lower – reuses Ethernet infrastructure
Higher – requires FC HBAs & switches
Complexity
Low – easy to deploy & manage
High – requires trained SAN admins
Best For
File servers, logs, home dirs, media
Databases, VMs, high-IOPS apps
HA / Redundancy
NIC bonding + RAID on NAS
Dual fabric, MPIO, multi-controller

## Slide 10
Advanced Enterprise Storage Features
Built-in capabilities that protect data, boost performance, and ensure business continuity.
RAID
Disk Failure Protection
RAID 1: Mirroring (exact copy)
RAID 5: Parity (1 disk fault tolerance)
RAID 6: Dual parity (2 disk tolerance)
RAID 10: Mirror + Stripe (highest perf)
Snapshots
Point-in-Time Recovery
Instant point-in-time copy of data
No performance impact during snapshot
Recover files in seconds, not hours
Used for backup and testing
Replication
Disaster Recovery
Synchronous: zero RPO (local)
Asynchronous: low RPO (remote site)
Active-Active: both sites serve data
Automated failover on site failure
Caching
Performance Acceleration
NVMe/SSD cache tier for hot data
Read cache: frequently accessed blocks
Write cache: battery-backed for safety
10x-100x IOPS improvement vs HDD

## Slide 11
Real-World Enterprise Storage Design
PRIMARY DATA CENTER
App / DB Servers
Windows + Linux VMs
SAN Switch A + B
Brocade Dual Fabric
FC SAN Array
Databases & VMs (32G FC)
NAS Array
File Shares & Logs (10G ETH)
Async
Replication
WAN / DWDM
DR / SECONDARY SITE
Standby Servers
Cold / Warm standby
SAN Switch A + B
Mirror of primary fabric
FC SAN Array (DR)
Replicated volumes (RPO < 15min)
NAS Array (DR)
Replicated file shares

## Slide 12
Key Takeaways
What you should walk away knowing
01
NAS = File-Based, Simple
NAS delivers shared file storage over Ethernet using NFS/SMB. Easy to deploy, cost-effective, ideal for file servers and collaboration.
02
SAN = Block-Based, High Perf
SAN presents raw block storage (LUNs) over dedicated Fibre Channel. The OS controls the file system. Best for databases and VMs.
03
Fibre Channel = The Transport
FC is the dedicated protocol for SAN networks — separate from Ethernet. Delivers 16-64 Gbps with sub-millisecond latency.
04
SAN Switches = The Fabric
SAN switches create the storage fabric. Zoning enforces access security. Multipathing ensures HA with automatic failover.
05
Storage = Critical Infrastructure
Without resilient storage (RAID, snapshots, replication), data is at risk. Enterprise storage is the backbone of data center resilience.
06
Choose the Right Architecture
NAS and SAN are complementary — enterprises use both. NAS for files, SAN for mission-critical block workloads.