## Slide 1
Enterprise Data Center
Storage Architecture
Understanding NAS, SAN, Fibre Channel, and SAN Switches
Presented by: Navdeep | Audience: Arun

## Slide 2
AGENDA
01
What is Storage in a Data Center?
02
Why Enterprises Use Dedicated Storage
03
Types of Storage Architectures (DAS / NAS / SAN)
04
NAS – Concepts, Architecture & Use Cases
05
SAN – Concepts, Architecture & Use Cases
06
Fibre Channel Overview
07
SAN Switches & Fabric
08
NAS vs SAN Comparison
09
Real-World Enterprise Storage Design
10
Summary & Key Takeaways

## Slide 3
What Is Storage in a Data Center?
Application Data
All business application records and operational data
Databases
Relational & NoSQL engines powering enterprise apps
Virtual Machines
VM disk images, snapshots, and VM state files
Logs & Backups
Audit trails, DR copies, and compliance archives
KEY CONCEPT
💾
STORAGE
Storage exists independently
from compute (servers).
Even if a server fails, data must
remain safe, accessible, and
consistent.

## Slide 4
Why Enterprises Use Dedicated Storage
🛡️
Data Survives Failures
Storage operates independently — server crashes do not destroy data
🔗
Shared Access
Multiple servers access the same datasets simultaneously
⚡
High Performance
Optimized I/O for databases, VMs, and high-transaction workloads
📈
Scalability
Expand capacity without disrupting running applications
🔒
Centralized Security
Unified access control, encryption, and audit logging
🛠️
Simplified Management
Single-pane-of-glass administration and monitoring
⚠ Local disks alone are not sufficient for enterprise workloads

## Slide 5
Types of Storage Architectures
Each architecture serves different performance, cost, and scalability needs
DAS
Direct Attached Storage
💻
✔ Fast, Simple
✘ No sharing, Limited scale
USE CASE
OS disks, Dev/Test
NAS
Network Attached Storage
🌐
✔ Easy sharing, Cost-effective
✘ File-level only, Ethernet overhead
USE CASE
File servers, Logs, Media
SAN
Storage Area Network
⚙️
✔ Block-level, High performance
✘ Complex, Higher cost
USE CASE
Databases, VMs, ERP

## Slide 6
Direct Attached Storage (DAS)
🖥 SERVER
CPU + RAM + OS
SATA/SAS →
💽 DISK ARRAY
SATA / SAS / NVMe
No Network
Speed
Extremely fast for a single server — direct bus connection
Isolation
Cannot be shared with other servers or clients
Scalability
Limited to physical bays inside/near the server
📌 Use Cases: OS boot drives | Small standalone applications | Dev/Test environments

## Slide 7
Network Attached Storage (NAS)
NAS provides file-level storage over a standard Ethernet network. It appears as a shared folder to all users and servers.
💻 Client A
💻 Client B
🖥 Server
🔀
Ethernet
Switch
🗄
NAS Controller
+ File System
Disks / RAID
NFS
Linux / Unix
SMB/CIFS
Windows
NFS/SMB requests travel over
standard Ethernet — no
specialized hardware needed.

## Slide 8
NAS – Features & Use Cases
🚀
Easy to Deploy
Plug into existing Ethernet — no specialized switches needed
🔗
Centralized File Sharing
All servers and users access the same shared directories
💰
Cost Effective
Leverages existing network infrastructure at low incremental cost
🔒
Access Control
Role-based permissions via Active Directory or LDAP integration
COMMON USE CASES
📁 File Servers
🏠 User Home Directories
📋 Application Logs
🎬 Media & Video Storage
📦 Backup Targets

## Slide 9
Storage Area Network (SAN)
SAN provides block-level storage over a dedicated high-speed network. Storage appears as a local disk to the server.
Block-Level Storage
Data is accessed in fixed-size blocks — like a raw local disk
Dedicated Network
SAN traffic travels on a separate Fibre Channel or iSCSI network
Server Controls FS
The server (not storage) formats and manages the file system
High Performance
Sub-millisecond latency, perfect for databases & VMs
SAN KEY CONCEPT
🖥 Server A → sees /dev/sdb
🖥 Server B → sees /dev/sdc
Storage Array | LUN Pool
Fibre Channel / iSCSI
Dedicated SAN Fabric

## Slide 10
SAN Architecture – Components & Data Flow
🖥 Server 1
HBA
🖥 Server 2
HBA
🖥 Server 3
HBA
🔀
SAN SWITCH
(FC Fabric)
Zoning
Multipath
Redundancy
🗄
Storage Array
Controllers
LUN 1
LUN 2
LUN 3
Fibre Channel / iSCSI
HBA → FC Cable → SAN Switch → Storage Controller → LUN assigned to server

## Slide 11
Understanding Block Storage
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Block 8
Block 9
Block 10
Block 11
Raw Block Pool (LUN)
OS formats block device → creates file system (NTFS / ext4 / XFS)
Sub-millisecond latency
Direct block access bypasses file-system overhead
Consistent IOPS
Predictable performance for OLTP and ERP workloads
OS-managed FS
Server applies NTFS, ext4, XFS — full control
Ideal for VMs
VMware VMFS, Hyper-V volumes run natively on SAN

## Slide 12
Fibre Channel (FC)
A dedicated, high-performance storage networking protocol — separate from Ethernet
16 Gbps
Standard enterprise
deployments
32 Gbps
High-demand
environments
64 Gbps
Next-gen, AI &
high-performance
🔵
Lossless Protocol
Guaranteed delivery — no dropped frames, critical for storage I/O
⚡
Ultra-Low Latency
Microsecond response times for OLTP databases
🔒
Dedicated Fabric
Traffic isolation — zero contention with IP/Ethernet networks
🔁
Multipath Support
Dual-fabric, redundant paths with automatic failover

## Slide 13
Fibre Channel – Key Components
🖥
HBA
Host Bus Adapter
Installed in the server. Connects to the FC network. Has a unique 64-bit WWPN identifier.
🔀
FC Switch
Fibre Channel Switch
Provides the storage fabric. Routes frames between hosts and storage using WWPN-based zoning.
🗄
Storage
Controller
Storage Array Controller
Manages disk pools, presents LUNs, handles RAID, caching, and replication.
🔗
Fiber
Optic Cable
OM4 / Single-Mode Fiber
Low-latency, high-bandwidth physical medium. Multi-mode OM4 up to 100m; Single-mode up to 10km.

## Slide 14
SAN Switches & Storage Fabric
🖥 Server 1
🖥 Server 2
🔀 FC Switch A
🔀 FC Switch B
🗄
Storage Array
Port A | Port B
Fabric A (Primary)
Fabric B (Redundant)
Zoning:
Controls which servers can see which LUNs. Enforced at switch level.
Multipathing:
Two independent fabrics → auto failover if primary path fails.
Vendors:
Brocade (HPE SAN) · Cisco MDS · Huawei OceanStor

## Slide 15
High Availability & Security in SAN
🔒 ZONING
Zone A (DB Server ↔ LUN-01, LUN-02)
🖥 DB Server → 🗄 LUN-01, LUN-02
No other server can see LUN-01/02
Zone B (App Server ↔ LUN-03)
🖥 App Server → 🗄 LUN-03
Completely isolated from Zone A
🔁 MULTIPATHING
🖥 Server
Path 1 (Active)
Path 2 (Standby)
🗄
Storage
If Path 1 fails
MPIO software detects failure and instantly switches I/O to Path 2 with zero data loss.

## Slide 16
NAS vs SAN – Side-by-Side Comparison
Criterion
NAS
SAN
Storage Type
File-level (NFS / SMB)
Block-level (LUN)
Network
Standard Ethernet (1/10/25 GbE)
Fibre Channel / iSCSI
Performance
Good – shared file workloads
Excellent – database / VM I/O
Complexity
Low – easy to deploy & manage
High – requires FC expertise
Cost
Lower CapEx & OpEx
Higher CapEx (HBA, FC switches)
Scalability
Moderate
Very High
Use Case
Files, logs, home dirs, media
Databases, VMs, ERP, OLTP
Protocol
NFS, SMB/CIFS
FC-SCSI, iSCSI, FCoE

## Slide 17
Advanced Enterprise Storage Capabilities
🛡️ RAID
• Redundant Array of Independent Disks
• RAID 5 / 6 – parity-based protection
• RAID 10 – mirroring + striping
• Survives single or dual disk failures
📸 Snapshots
• Point-in-time copy of data
• Near-instant recovery from logical errors
• Space-efficient (copy-on-write / redirect-on-write)
• RPO near zero for DB recovery
🔄 Replication
• Synchronous – zero data loss (RPO=0)
• Asynchronous – low bandwidth DR replication
• Cross-site to DR / Azure / cloud
• Critical for Business Continuity
⚡ NVMe Cache
• NVMe SSD tier for hot data acceleration
• Read cache + write buffer combination
• Automatic data tiering (hot/warm/cold)
• 10–100× throughput improvement

## Slide 18
Typical Enterprise Storage Design
Resilient, tiered architecture combining NAS and SAN with DR replication
PRIMARY DATA CENTER
🖥 DB Svr
🖥 App Svr
🖥 Web Svr
FC Sw A
FC Sw B
SAN
(Databases)
NAS
(Files)
Async Replication →
DR SITE
🗄
DR Storage
Replica of SAN
+ NAS volumes
RTO: < 4hr
RPO: < 15min
Dual SAN switches eliminate single points of failure · NAS for files · SAN (FC) for databases · DR replication ensures business continuity

## Slide 19
Why Enterprise Storage Matters
🛡️
99.999%
Availability SLA
Data Protection
RAID, snapshots, and replication protect against hardware failure, human error, and site disasters.
⚡
<1ms
SAN Latency
Application Performance
Block storage with NVMe caching delivers consistent sub-millisecond I/O for databases and VMs.
🕐
RTO < 4h
Recovery Objective
Minimized Downtime
DR replication ensures rapid recovery — revenue loss from downtime avoided.
📈
PB Scale
Capacity
Future Growth
Enterprise SAN and NAS scale to petabytes without disrupting production services.

## Slide 20
Key Takeaways
1
NAS is file-based, simple to deploy, and ideal for file sharing over Ethernet using NFS or SMB/CIFS.
2
SAN is block-based, high-performance, and essential for databases, VMs, and enterprise applications.
3
Fibre Channel provides a lossless, dedicated, ultra-low-latency storage network at 16/32/64 Gbps.
4
SAN switches create a resilient fabric with zoning for security and multipathing for high availability.
5
Enterprise storage = RAID + Snapshots + Replication + Caching — the foundation of resilient data centers.
Enterprise Storage = The Foundation of Data Center Resilience

## Slide 21
Thank You
Enterprise Data Center Storage Architecture
Questions?
Navdeep · Presented to: Arun